## Slide 1: ELEC 3300 Proposal
Ieong, Zi Liang jason (zljieong)
Yim Man Chak (mcyim)

## Slide 2: Project Idea
Reinventing remote robot with 3D input

## Slide 3: Ideas Behind…
References:
Right: The Best Raspberry Pi 3 Kits for Robotics
Left: RC King 27Mhz Remote Control, Remote Controller Transmitter Controller Accessories for Kids Ride On Car Replacement Parts
Traditional robots with 2 wheels are capable of only turn left/right, forward/backward
2D input

## Slide 4: Ideas Behind…
References:
Right: How to build an Omni Wheels Robot
Left: Motion-sensing game controllers explained
Omni Wheels Robot capable of rotating around Z-axis and forward/backward towards any direction
3D motion input?

## Slide 5: Project Deliverables
References:
Right: How to build an Omni Wheels Robot
Left: Motion-sensing game controllers explained
Omni Wheels Robot capable of rotating around Z-axis and forward/backward towards any direction
3D motion input?
🎮
Handheld remote controller with motion detection
🤖
Omni Wheels Robot
with 3 wheels
Bluetooth

## Slide 6: Project Deliverables
🎮
Handheld remote controller with motion detection
🤖
Omni Wheels Robot
with 3 wheels
Bluetooth

## Slide 7: Project Design
Remote 🎮
Robot 🤖

## Slide 8: Functional Requirements
Communication
Motion Sensing
Closed loop motion control

## Slide 9: Motion Sensing
🎮
Hardware Used
  MPU6050
  Known issues:
    Gyroscope drifts
    Accelerometer unstable
Software solution:
  Complementary Filter / Kalmen Filter
Image source: https://robottini.altervista.org/kalman-filter-vs-complementary-filter

## Slide 10: Communication
🎮
🤖
Target: wireless control
Options: WIFI / Bluetooth
  Bluetooth is good enough
  Consumes less power and computational power
Hardware Used:
  HC05
Protocol:
  UART

## Slide 11: Closed Loop Motion Control
🤖
Mechanical problems:
  Each Omni wheel introduce error
Hardware and Software solution:
  Encoder
    Individual PID control
  MPU6050
    Global speed control
Image source: https://www.roboteq.com/images/article-images/frontpage/wheel-rotations.jpg

## Slide 12: Additional Features
🎮
🤖
Battery
Then it’s truly handheld
Vibration Motor
Alerting user of events, e.g., low battery, car collision
I2C LCD & Buttons
Interaction with user and provide remote and car info
RGB LED
Better user experience
IR pulse sensor
User pulse checking
Battery
No more cable!
3 TOF Sensors
Distance detection for preventing wall collision
6 RGB LEDs
Better user experience
EEPROM
Storing calibration

## Slide 13: Challenges
Difficulties & limitations

## Slide 14: Difficulties & Limitations
🎮: Control method can be difficult to adapt
🎮: Limited control distance due to short BT coverage
🤖: No camera (difficult for analysis and self-positioning)
🤖: Difficult to evaluate control performance

## Slide 15: Thank you!